## Slide 1: TapPrints: Your Finger Taps Have Fingerprints
Presented by: Tom Staley

## Slide 2: About
Paper by
  Emiliano Miluzzo
  Alexander Varshavsky
  Suhrid Balakrishnan
  Romit Roy Choudhury
Originally presented at MobiSys2012, June 27, 2012

## Slide 3: Introduction
Determining location of screen taps using accelerometer and gyroscopes
Could lead to attackers using this info to track inputs
“TapPrints- a framework for inferring location of taps on mobile devices”

## Slide 4: Current State of Sensors
Mobile sensors becoming more powerful
Many types of data: patient monitoring, localization, context-awareness, etc.
Rumored that insurance companies are trying to use dietary patterns to determine cost and coverage of policies

## Slide 5: Using Gyroscopes

## Slide 6: TapPrints
Implemented on Google Nexus S, Apple iPhone 4, Samsung Galaxy Tab 10.1
Over 40,000 taps collected from 10 users over 4 weeks
80-90% accuracy, enough to guess a password

## Slide 7: How Data Could be Used
Attackers can improve odds by:
  Applying a spellchecker to guess unknown words
  Narrowing search to email addresses in contact list if the email application is running
Data can be protected by:
  Using a rubber case to absorb motions
  Switching to swiping-based keyboards

## Slide 8: Is this a Threat?
Attacks could be disguised as any app available on the market
Only sensor that requires permission is location
Accelerometer and gyroscope largely ignored due to gaming

## Slide 9: How to Differentiate Taps

## Slide 10: Recognizing Taps
TapPrints has to be trained to recognize taps
Different methods:
  k-Nearest Neighbor
  Multinomial Logistic Regression
  Support Vector Machines
  Random Forests
  Bagged Decision Trees
Combine all methods at end to get best results

## Slide 11: Collecting Data
Used four methods:
  Icon Taps
  Sequential Letters
  Pangrams
  Repeated Pangrams

## Slide 12: Icon Taps
Averages:
  iPhone- 78.7%
  Nexus- 67.1%
Random guess is only 5%

## Slide 13: Repetitions
Stabilizes at 20 taps/icon
70% accuracy reached at 12 taps
Attackers could disguise as a game
Could also pre-train to recognize other users’ taps

## Slide 14: Letter Tapping
Harder than icon taps because letters are smaller and have less separation
Average prediction is 65.11% after training using pangrams
Random guess is only 3.8%

## Slide 15: Letter Confusion
Mostly limited to surrounding letters
Could be used in a dictionary search to guess words
Some letters better than others, e.g. E vs. W

## Slide 16: Example of Pangram

## Slide 17: Sequential Letters

## Slide 18: Letter Repetition
More repetitions required because of smaller areas
150 taps to reach 50%

## Slide 19: Sensor Efficacy

## Slide 20: Possible Solutions
Pause sensors when typing
Agreements with developers to hold them accountable
Have users grant permission to use sensors
Rubber cases to absorb motion
Swiping-based keyboards

## Slide 21: Conclusion
Attackers can use software to track user input
TapPrints is just an early implementation
In future, software will be much more powerful

## Slide 22: Bibliography
Miluzzo, Emiliano, Alexander Varshavsky, Suhrid Balakrishnan, and Romit Roy Choudhury. "Tapprints: Your Finger Taps Have Fingerprints." MobiSys '12 Proceedings of the 10th International Conference on Mobile Systems, Applications, and Services. MobiSys 2012, United Kingdom, Low Wood Bay, Lake District. New York: ACM, 2012. 323-36. Print.